## Slide 1: COMPUTERIZED METHODS OF LAYOUT DESIGN
In Computerized methods of Layout Design, we have two types of Algorithms, i.e:
  Constructive Type Algorithm
  Improvement Type Algorithm

## Slide 2: COMPUTERIZED METHODS OF LAYOUT DESIGN (CONT..)
The key element of Computerized Layout planning is the representation & manipulation of the following three types of information:
  Numeric information: Space required for an activity, total flow b/w two activities
  Logic information: Preferences of the designer, i.e., the activity relationship chart
  Graphical information: Drawing of the block plan

## Slide 3: COMPUTERIZED METHODS OF LAYOUT DESIGN (CONT..)
Constructive Algorithms are of following types:
  Automated Layout Design Program (ALDEP)
  Computerized Relationship Planning (CORELAP)
The most famous type in Improvement types Algorithms is;
    1. Computerized Relative Allocation of Facilities Technique (CRAFT).

## Slide 4: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)
CRAFT is more popular than the other computer based layout procedures.
It is improvement algorithm & starts with an initial layout & proceeds to improve the layout by interchanging the departments pair wise to reduce the total material transportation cost
It does not give the Optimal Layout; but the results are good & near optimal, which can be later corrected to suit the need of the layout planner

## Slide 5: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Features of CRAFT:
It attempts to minimize transportation cost, where Transportation cost = flow x distance x unit cost
It Requires assumptions that:
(1) move cost are independent of the
equipment utilization &
(2) move costs are linearly related to the
length of the move

## Slide 6: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Features of CRAFT:
Distance matrix used is the rectilinear distance b/w department centroids
CRAFT being a path-oriented method, the final layout is dependent on the initial layout. Therefore, a number of initial layouts should be used as input to the CRAFT
CRAFT allows the use of dummy departments to represent fixed areas in the layout

## Slide 7: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Input Requirements of CRAFT:
6. CRAFT input requirements are as follows:
  Initial Layout
  Flow Data
  Cost per unit distance
  Total number of departments
  Fixed departments & their location
  Area of departments

## Slide 8: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Procedure adopted for using CRAFT:
Determine the department centroids
Calculate rectilinear distance b/w centroids
Calculate transportation cost for the layout
Consider department exchanges of either equal area departments or of departments sharing common border
Determine transportation cost of each department interchange

## Slide 9: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Procedure adopted for using CRAFT:
Select & implement the departmental interchange that offers the greatest reduction in transportation cost
Repeat the procedure for the new layout until no interchange is able to reduce the transportation cost

## Slide 10: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Major Disadvantage of Using CRAFT:
Because the basis is the cost of materials handling, only production departments are considered.
An initial idea of the layout is required. Therefore the technique only applies to the modification of an existing layout or new layouts where the outline shape is known

## Slide 11: COMPUTERIZED RELATIVE ALLOCATION OF FACILITIES TECHNIQUE (CRAFT)..Cont..
Major Disadvantage of Using CRAFT:
The Distance b/w the departments is taken as straight lines where as in practice movement is usually rectangular along orthogonal lines

## Slide 12: CRAFT: ILLUSTRATIVE Example
Example 1 Consider the following layout problem with unit cost matrix (as in table1.2). Use CRAFT algorithm to obtain layout. The initial layout is shown in table 1.1 & the flow matrix in table 1.3
7 7
7
7
7 7
Table 1.1. Initial Layout
Assume the unit cost per Transfer to be 1
A | B
D | C

## Slide 13: CRAFT: ILLUSTRATIVE Example (cont..)
Table: 1.2.Flow Matrix
Department | A | B | C | D
A |  | 30 | 25 | 45
B | 20 |  | 15 | 20
C | 10 | 20 |  | 10
D | 100 | 10 | 5 | 

## Slide 14: CRAFT: ILLUSTRATIVE Example
Solution:
Centroids of the department for given initial layout are as:
(XA, YA) = 3.5, 10.5
(XB, YB) = 10.5, 10.5
(XC, YC) = 10.5, 3.5
(XD, YD) = 3.5, 3.5

## Slide 15: CRAFT: ILLUSTRATIVE Example (Cont..)
Solution:
Using the Rectilinear Distance, we draw the distance matrix as shown in table 1.3
Table. 1.3: Distance Matrix
Department | A | B | C | D
A | 0 | 7 | 14 | 7
B | 7 | 0 | 7 | 14
C | 14 | 7 | 0 | 7
D | 7 | 14 | 7 | 0

## Slide 16: CRAFT: ILLUSTRATIVE Example (Cont..)
Solution:
Total material handling cost is calculated as by:
Total cost = Flow x Distance x Unit cost
Fig.1.4. Total Cost Matrix
Department | A | B | C | D | Cost
A | 0 | 210 | 350 | 315 | 875
B | 140 | 0 | 105 | 280 | 525
C | 140 | 140 | 0 | 70 | 350
D | 700 | 140 | 35 | 0 | 875
Total Cost |  |  |  |  | 2625

## Slide 17: CRAFT: ILLUSTRATIVE Example (Cont..)
Solution:
4. Departmental Interchanges:
Consider various departmental interchanges for improvement
Departmental interchange is possible for
departments having common boundary or
equal area

## Slide 18: CRAFT: ILLUSTRATIVE Example (Cont..)
Solution:
4. Departmental Interchanges:
Possible Departmental Interchanges are shown in table 1.5
Table 1.5
Departmental pair | Reason
A-B | Common border & Equal area
A-C | Equal area
A-D | Common border & Equal area
B-C | Common border & Equal area
B-D | Equal area
C-D | Common border & Equal area

## Slide 19: CRAFT: ILLUSTRATIVE Example (Cont..)
Solution:
5. For the purpose of calculating material handling cost, interchange would mean change in the centroid. In the same way as we calculated the total cost for the initial layout, we calculate the total cost for each of the possible interchanges, & select the layout that gives the least total cost