## Slide 1: AUTOMATED LAYOUT DESIGN PROGRAM (ALDEP)
ALDEP is basically a construction algorithm, but it can also be used to evaluate two layouts
It uses basic data on facilities & builds a layout by successively placing the layout using relationship information b/w the departments

## Slide 2: AUTOMATED LAYOUT DESIGN PROGRAM (ALDEP)…cont…
Basic Inputs to ALDEP:
Length & width of facility
Area of each department
Minimum Closeness Preference (MCP) Value
Sweep width
Relationship chart showing the closeness rating
Location & size of any restricted area

## Slide 3: AUTOMATED LAYOUT DESIGN PROGRAM (ALDEP)…cont…
Procedure Adapted for using ALDEP :
Step#01: Input the following
  Length & width of facility
  Area of each department
  Minimum Closeness Preference (MCP) Value
  Sweep width
  Relationship chart showing the closeness rating
  Location & size of any restricted area

## Slide 4: AUTOMATED LAYOUT DESIGN PROGRAM (ALDEP)…cont…
Procedure Adapted for using ALDEP :
Step#2: One department is selected randomly & placed in the layout
Step#3: In this step, the algorithm uses minimum closeness required b/w departments for the selection of departments to be placed with an earlier placed department.
Select the department having maximum closeness rating. If there is no department having minimum closeness preference then any dept that remains to be placed is selected

## Slide 5: AUTOMATED LAYOUT DESIGN PROGRAM (ALDEP)…cont…
Procedure Adapted for using ALDEP :
Step#4: If all the departments are placed in the layout, go to step#5. else go to step#3
Step#5: Compute the total score of the layout
Step#6: If the total score required is acceptable score, then go to step#7, else go to step#2
Step#7: Print the current layout & the corresponding score

## Slide 6: ALDEP: ILLUSTRATIVE Example
Example 2: Develop a layout for the following problem. Layout & area requirements are shown in Table2.1
Table.2.1
Department | Area (sq.ft) | No. of unit squares
1 | 1200 | 30
2 | 800 | 20
3 | 600 | 15
4 | 1200 | 30
5 | 800 | 20
6 | 1200 | 30
7 | 1200 | 30
Total | 7000 | 175

## Slide 7: ALDEP: ILLUSTRATIVE Example
Solution: Assume One square in the layout to be equal 40 sq.ft.
No. of unit squares for dept = dept.area in sq.ft/area per square
Let the size of layout be 15x12, & the sweep width be 2 (this means that we will fill 2 columns simultaneously).
The Relationship chart for the example is follows:
Department | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 |  | E | O | I | O | U | U
2 | E |  | U | E | I | I | U
3 | O | U |  | U | U | O | U
4 | I | E | U |  | I | U | U
5 | O | I | U | I |  | A | I
6 | U | I | O | U | A |  | E
7 | U | U | U | U | I | E | 

## Slide 8: ALDEP: ILLUSTRATIVE Example
Solution: Let department 2 be selected. Number of unit squares in dept 1 be 20. now 20 square units are filled in 15 x 12 grid as shown in table2.2
Since minimum closeness b/w departments required for selection of department is I=4
Scan the relationship chart randomly to find the departments having closeness rating of 4 or greater with department 2

## Slide 9: ALDEP: ILLUSTRATIVE Example
Solution:
For the above case closeness rating for the pairs (1-2)=16, (2-5)=4, & (2-6)=4
Select any dept, say dept 1. Place dept 1 in the layout in a serpentine pattern as shown in table 2.3
Repeat the above procedure to get the final layout as shown in table 2.4

## Slide 10: ALDEP: ILLUSTRATIVE Example
Solution:
After the final layout is obtained, the score is calculated.
The score is the sum of the closeness ratings of all the neighboring departments, see table 2.5
From the above layout the score is 2 x110 = 220
A further iteration should be carried out to check if a better score can be achieved