Experiment

INTRODUCTION

Bending moment in physics is an example of an internal force that is induced in a structure when loads are applied to that structure. Loading tends to cause failure in two main ways:

- by shearing the beam across its cross-section.

- by bending the beam to an excessive amount.

A bending moment may be defined as "the sum of turning forces about that section of all external forces acting to one side of that section”. Moments, at any point, are calculated by multiplying the magnitude of the external forces (loads or reactions) by the distance between the point at which moment is being determined and the point at which the external forces (loads or reactions) are being applied

The objective of this experiment are to show that at any section of a beam subjected to transverse loads, the shearing force is define as the algebraic sum of the transverse component of force located at one side of the section. In addition, the bending moment is defined as the algebraic sum of the moment of the force to one side of the section.

The applications of the experiment are to study about how to establish the shear and moment for bean and shaft. Beam and shaft are important structural and mechanical element in engineering.

THEORY

Consider the cantilever beam subjected to a number of transverse loads W located at distance x, as show in figure.

Note the sign conversation used

Cantilever Beam Loading                                 Shearing Force and Bending Moment Sign Convention:

At any transverse section X-X:

- the shearing force:		Q= ∑W=W3-W2-W1

- the bending moment:	M=∑WX=W3x3-W2x2-W1x1

PROCEDURE

Apparatus

- The beam is checked whether it is in equilibrium position when without a load applied to the beam.

- The support tension adjusted if necessary.

- The load is attached to hanger 2 and weights to the beam at position xi, and weight is added to hanger 3 and 4 until the beam return to equilibrium position.

- The experiment is repeated with weights at position x2 and x3.

- The value is recorded for each position of the load W

- The experiment is continued with two addition weight value are 2N and 3N.

RESULT

Load: 100 gram

| Distance (m) | Experimental Value | Theoretical Value | %Error |
| --- | --- | --- | --- |
|  | W1(N) | W2(N) | W2 x a (Nm) | Qx(N) | Mx(Nm) | W1 & Q | W2 x a &Mx |
| x1 | 0.981 | 1.4715 | 0.14715 | 0.981 | 0.14715 | 0 | 0 |
| x2 | 0.981 | 0.981 | 0.0981 | 0.981 | 0.0981 | 0 | 0 |
| x3 | 0.981 | 0.4905 | 0.04905 | 0.981 | 0.04905 | 0 | 0 |

Load: 200 gram

| Distance (m) | Experimental Value | Theoretical Value | %Error |
| --- | --- | --- | --- |
|  | W1(N) | W2(N) | W2 x a (Nm) | Qx(N) | Mx(Nm) | W1 & Q | W2 x a &Mx |
| x1 | 1.962 | 2.943 | 0.2943 | 1.962 | 0.2943 | 0 | 0 |
| x2 | 1.962 | 1.962 | 0.1962 | 1.962 | 0.1962 | 0 | 0 |
| x3 | 1.962 | 0.981 | 0.0981 | 1.962 | 0.0981 | 0 | 0 |

Load: 300 gram

| Distance (m) | Experimental Value | Theoretical Value | %Error |
| --- | --- | --- | --- |
|  | W1(N) | W2(N) | W2 x a (Nm) | Qx(N) | Mx(Nm) | W1 & Q | W2 x a &Mx |
| x1 | 2.943 | 4.4145 | 0.44145 | 2.943 | 0.44145 | 0 | 0 |
| x2 | 2.943 | 2.943 | 0.2943 | 2.943 | 0.2943 | 0 | 0 |
| x3 | 2.943 | 1.4715 | 0.14715 | 2.943 | 0.14715 | 0 | 0 |

x1 = 0.15m

x2 = 0.10m

x3 = 0.05m

Shearing force and bending moment diagrams

Load: 100 gram

x1=0.15m

Load: 100 gram

x2=0.10m

Conclusions

In this experiment, we need to consider bending moment and shear force need to be considered to make the system in equilibrium. We also conclude that the shorter the perpendicular distance to the load, the system will produce less bending moment which is preferable and more stable.

# Text boxes

0.15m

W1

Mx

-0.981

V(N)

x(m)

Shearing force diagram

0.15

M(N.m)

x(m)

-0.14715

-0.981x

0.15

Bending moment diagram

0.10m

W1

Mx

-0.981

V(N)

x(m)

Shearing force diagram

0.10

M(N.m)

x(m)

-0.0981

-0.981x

0.10

Bending moment diagram