## Slide 1: Material Handling Cost
Main costs involved in designing & operating a material handling system are:
Equipment Cost; this comprises the purchasing of equipment, & auxillary components & installation
Operating Cost; which include maintenance, fuel, & labor cost, consisting of both wages & injury compensation
Unit Purchase Cost; which is associated with purchasing the pallets & containers
Cost due to packaging & damaged material

## Slide 2: CONSIDERATIONS IN MATERIAL HANDLING SYSTEM DESIGN
1. Material Characteristics
Category | Measures
Physical state Size Weight Shape Condition Safety risk and risk of damage | Solid, liquid, or gas Volume; length, width, height Weight per piece, weight per unit volume Long and flat, round, square, etc. Hot, cold, wet, etc. Explosive, flammable, toxic; fragile, etc.

## Slide 3: CONSIDERATIONS …CONT.
2. Flow rate
Manual handling
Hand trucks
Powered trucks
Unit load AGV
Conveyors
Conveyors
AGV train
High
Low
Long
Short
Move Distance
Quantity of
material
moved

## Slide 4: CONSIDERATIONS …CONT.
3. Plant Layout
Layout Type | Characteristics | Typical MH Equipment
Fixed – position Process Product | Large product size, low production rate Variation in product and processing, low and medium production rates Limited product variety, high production rate | Cranes, hoists, industrial trucks Hand trucks, forklift trucks, AGVs Conveyors for product flow, trucks to deliver components to stations.

## Slide 5: PRODUCTIVITY RATIOS
Productivity Ratios are used as indicators of the Performance of a system
These ratios are monitored periodically to be sure that their values are within acceptable tolerances
Though some ratios given later, do not specifically address productivity associated with material handling, all the ratios stated here for completeness

## Slide 6: PRODUCTIVITY RATIOS (Cont..)
Material-Handling-Labor (MHL) Ratio
= Personnel assigned to Material Handling/
Total Operating Personnel
- The ratio should be less than 1, & a Reasonable value would be less than 0.30 in a plant, while in a warehouse a higher value should be expected

## Slide 7: PRODUCTIVITY RATIOS (Cont..)
Handling Equipment Utilization (HEU) Ratio
= items (or load weight) moved per hour/ theoretical capacity
- Ideally, the ratio should be close to 1.0; however, equipment breakdown, poor scheduling, poor housekeeping & building geography can reduce the load movement

## Slide 8: PRODUCTIVITY RATIOS (Cont..)
3. Storage Space Utilization (SSU) Ratio
= Storage Space Occupied/
total available storage space
- A value close to 1 indicates assignment of appropriate space for the storage activities

## Slide 9: PRODUCTIVITY RATIOS (Cont..)
Aisle Space Percentage (ASP)
= Space occupied by Aisles/
Total Space
ASP should have a value b/w 0.10 & 0.15

## Slide 10: PRODUCTIVITY RATIOS (Cont..)
Movement/Operation (MO) Ratio
= number of moves/
number of productive operations
The ratio indicates the amount of material handling performed.
The moves involved may consist of material moved from receiving, from storage to an operation & back to storage, & so on.
A high value indicate room for improvement

## Slide 11: PRODUCTIVITY RATIOS (Cont..)
Manufacturing Cycle Efficiency (MCE)
= Time in actual production operations (machine time)/
time in production department
For increasing machine utilization, the delay should be eliminated or at least minimized
The performance index should be observed over a time period for consistency

## Slide 12: PRODUCTIVITY RATIOS (Cont..)
Damaged Load (DL) Ratio
= Number of damaged loads /
Total number of Loads
The ratio measures the quality performance of MH Personnel
Damaged to the loads during receiving, in-process movement, & shipping should be minimized

## Slide 13: PRODUCTIVITY RATIOS (Cont..)
Energy Ratio
= Total BTU consumption in the warehouse/
Warehouse space
The energy ratio measures the efficiency of heating & cooling operations
Some of the ways in which ratio can be improved are reducing heating & cooling of a portion of the warehouse in which there are no workers, turning lights off when not needed, & using lights on moving vehicles rather than permanent lighting

## Slide 14: EQUIPMENT USED FOR MH
Equipment Types:
The equipment can be characterized by the area it is intended to serve:
Between fixed points over a fixed path
  Belt conveyor
  Roller conveyor
  Chute conveyor
  Slat conveyor
  Screw Conveyor
  Chain conveyor
  Overhead monorail conveyor
  Trolley conveyor
  Wheel conveyor
  Tow conveyor
  Bucket conveyor
  Cart-on-track conveyor
  Pneumatic tube conveyor

## Slide 15: EQUIPMENT USED FOR MH (Cont..)
Belt conveyor
Roller Conveyor
Chute conveyor
Chain conveyor
Screw Conveyor
Slat Conveyor
1. Between Fixed Points & Over fixed path

## Slide 16: EQUIPMENT USED FOR MH (Cont..)
1. Between Fixed Points & Over fixed path
Trolley Conveyor
Overhead monorail conveyor
Wheel Conveyor
Tow conveyor
Bucket
conveyor

## Slide 17: EQUIPMENT USED FOR MH (Cont..)
Between Fixed Points & Over fixed path
Cart-on-Track Conveyor

## Slide 18: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
2. Over Limited Areas
  Hoists
  Overhead cranes
  Hydraulic scissors lift

## Slide 19: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
2. Over Limited Areas
Hoist
Overhead crane
Hydraulic scissor lift

## Slide 20: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
  Hand cart/Truck
  Tier plate form truck
  Hand lift truck/pallet jack
  Power driven hand truck
  Power driven plat form truck
  Fork lift truck
  Narrow aisle truck
  Tractor-trailer train
  Material lift
  Drum truck
  Drum lifter
  Dolley
  4. AGVS

## Slide 21: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
Hand truck
Tier platform truck
Hand lift truck

## Slide 22: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
Power driven platform truck
Power driven hand truck

## Slide 23: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
Fork lift tuck
Narrow aisle truck

## Slide 24: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
Tractor Trailer Train
Material lift

## Slide 25: EQUIPMENT USED FOR MH (Cont..)
Equipment Types:
3. Over Large Areas
Drum Truck
Drum Lifter
Dolly